## Slide 1
Cambridge International AS Level Computer Science (9618) – Revision Notes
Networking and Communication Systems
This pack is intended for students to who are taking CIE AS Level in Computer Science, either in preparation for their AS exam, or more likely alongside year 2 of the course to improve fluency, recall and pace on AS topics. It could be used as lesson starters, or supplied to students for independent use.

## Slide 2
Networking and Communication Systems
A LEVEL COMPUTER SCIENCE
Chapter
2

## Slide 3
Chapter
Outline
History and Advantages of Networking
2.1
Designs and Structures of Network Topologies
2.2
Network Transmission Media
LAN
Hardware
components
2.4
2.3
Ethernet Technology and Standards
2.5
Architecture of the Internet
2.6
Internet-Based Applications
2.7
IP Addressing and Network Identification
2.8
Domain Naming Systems (DNS)
2.9

## Slide 4
2.1 History and Advantages of Networking
Wide Area Network
In the past, this is how a computer can be accessed by multiple users.
Mainframe Computer
Terminal

## Slide 5
Mainframe Computer
Terminal
Wide Area Network
WAN is developed to allow computers in different organisations to be networked.
Mainframe Computer
Terminal
Mainframe Computer
Terminal
Mainframe Computer
Terminal
Mainframe Computer
Terminal
In a WAN, computers can be thousands of kilometers apart.
2.1 History and Advantages of Networking

## Slide 6
Wide Area Network
WAN is developed to allow computers in different organisations to be networked.
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
2.1 History and Advantages of Networking

## Slide 7
Benefits of a WAN
  A task could be executed on a distant computer equipped with the necessary software.
  An archived dataset located on a remote computer could be retrieved.
  Information could be electronically sent to a user on a computer situated remotely.
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
2.1 History and Advantages of Networking

## Slide 8
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Ownership won't be with the organization; instead, leasing from a public switched telephone network company (PSTN) will occur. PSTN will offer an exclusive communication link.
Fibre-optic cable will serve as the transmission medium.
Communication inside the WAN will happen between switches.
Characteristics of a WAN
No end system is connected directly to the WAN.
2.1 History and Advantages of Networking

## Slide 9
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network
WAN
  The 1980s saw the advent of personal computers, altering computing dynamics.
  Users in organisations could have personal computers on their desks.
  Computers could operate standalone or be networked in a local area network.
2.1 History and Advantages of Networking

## Slide 10
Benefits of a LAN
By installing application software on an application server linked to the LAN, the cost of installing it on every individual PC can be minimized.
Application server
File server
2.1 History and Advantages of Networking

## Slide 11
Benefits of a LAN
By installing application software on an application server linked to the LAN, the cost of installing it on every individual PC can be minimized.
Application server
File server
Connecting a file server to the LAN enables users to store larger files and facilitates file sharing among users.
2.1 History and Advantages of Networking

## Slide 12
Benefits of a LAN
2.1 The evolution of the purpose and benefits of networking
By installing application software on an application server linked to the LAN, the cost of installing it on every individual PC can be minimized.
Application server
File server
Connecting a file server to the LAN enables users to store larger files and facilitates file sharing among users.
Organisational managers could utilize electronic mail for communication with staff, replacing the traditional practice of distributing paper memos.
2.1 History and Advantages of Networking

## Slide 13
Characteristics of a LAN
Application server
File server
  Used by an organization or company at a specific site or branch.
  Ownership rests with the organization or company.
  Utilises twisted-pair cables or Wi-Fi as the transmission medium.
  Each LAN will have a device to link to other networks.
  Features end-systems, comprising user systems or servers, linked to the LAN.
2.1 History and Advantages of Networking

## Slide 14
Differences between LAN and WAN
Local Area Network (LAN) | Wide Area Network (WAN)
Ownership rests with the organization or company. | Ownership won't be with the organization; instead, leasing from a public switched telephone network company (PSTN) will occur. PSTN will offer an exclusive communication link.
Utilises twisted-pa﻿ir cables or Wi-Fi as the transmission medium. | Fibre-optic cable will serve as the transmission medium.
Features end-systems, comprising user systems or servers, linked to the LAN. | No end system is connected directly to the WAN.
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Application server
File server
2.1 History and Advantages of Networking

## Slide 15
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
Wide Area Network (WAN)
Wide Area Network (WAN)
Wide Area Network (WAN)
The fundamental purpose and advantages of networking remain consistent, but their extent and range have expanded significantly. Notably, individuals now enjoy complete network access through their personal devices.
Internet (Interconnected Networks)
2.1 History and Advantages of Networking

## Slide 16
The client-server model
serve
obtain
a service
Application server
File server
Definition: An architecture where a client runs an application provided by a server on a network.
Nowadays, the client constitutes a web browser linked to the internet, while the server embodies a web server hosted on the internet.
james gan
2.1 History and Advantages of Networking

## Slide 17
The client-server model
Type 1: Thin-client
Step 1: Choose an application to run on the server.
Step 2: Sends input data to the server when requested by the application.
Step 3: Receives output from the application.
2.1 History and Advantages of Networking

## Slide 18
The client-server model
Type 2: Thick-client
Step 1: Choose an application to run on the server.
Perform certain processing tasks before sending the request to the server and can also handle additional processing after receiving the output from the application.
The client might also downloads the application from the server and then runs the application locally on its own device.
2.1 History and Advantages of Networking

## Slide 19
Example: Thick Client Preprocessing
Submitting an online form to calculate the total cost of items you want to purchase.
As you fill in the quantities and prices of items, your web browser (the client) performs calculations to calculate the subtotals for each item based on the quantity and price you entered.
Data sent to server
2.1 History and Advantages of Networking

## Slide 20
Example: Thick Client Preprocessing
Submitting an online form to calculate the total cost of items you want to purchase.
As you fill in the quantities and prices of items, your web browser (the client) performs calculations to calculate the subtotals for each item based on the quantity and price you entered.
The server then generates the final output, which includes the total cost and any other relevant information.
Data sent to server
2.1 History and Advantages of Networking

## Slide 21
Example: Thick Client Preprocessing
Submitting an online form to calculate the total cost of items you want to purchase.
As you fill in the quantities and prices of items, your web browser (the client) performs calculations to calculate the subtotals for each item based on the quantity and price you entered.
The server then generates the final output, which includes the total cost and any other relevant information.
Data sent to server
Raw data sent back
Once your browser receives the server's response, it may perform additional client-side processing to display the server's output in a user-friendly way.
17.99
2.1 History and Advantages of Networking

## Slide 22
The client-server model is the choice for the following circumstance:
The server holds a database that the client system can access.
The server hosts a web application that enables the client system to search for or occasionally provide information.
The server hosts a web application that enables the client system to conduct e-commerce or financial transactions.
2.1 History and Advantages of Networking

## Slide 23
Peer-to-peer model
Rather than relying on a single server that multiple clients access, a peer-to-peer network functions by having each peer store some files.
This setup allows every peer to act both as a client , requesting files from other peers, and as a server, providing requested files for download to other peers.
2.1 History and Advantages of Networking

## Slide 24
Comparing the advantages
Client-Server Model | Peer-To-Peer Model
It enables an organization to manage and regulate the downloading and utilization of files. | It prevents network congestion when multiple clients are trying to download files simultaneously.
Files can be safeguarded against malware attacks more effectively as they are stored on a single server that undergoes regular scanning using suitable anti-virus software. | Segments of a file can be downloaded individually.
 | The file segments are accessible from multiple hosts.
Application server
File server
2.1 History and Advantages of Networking

## Slide 25
Subtopic 1
Definition
2.2 Designs and Structures of Network Topologies
Network topology refers to the physical or logical layout of devices and their connections within a network. It defines how data flows and devices communicate.
Point-to-point
Bus
Mesh
Star
Overview
James Gan

## Slide 26
Subtopic 1
Topology
Before learning about topologies, we need to know what are the data transmission modes and methods.
Data Transmission Modes
Simplex
Half Duplex
Full Duplex
Data flow is one-way only.
Data flow in two ways but not at the same time.
Data flow in two way but at the same time.
2.2 Designs and Structures of Network Topologies

## Slide 27
Subtopic 1
Topology
Before learning about topologies, we need to know what are the data transmission modes and methods.
Data Transmission Methods
Broadcast
Multicast
Unicast
One-to-all communication
One to many communication
Data
Data
Data
Data
Data
One-to-one communication
Data
Data
2.2 Designs and Structures of Network Topologies

## Slide 28
Subtopic 1
Point-to-Point Topology
Point-to-point topology is a network configuration where two devices are directly connected to each other, forming a dedicated communication link between them.
Modes
Methods
Simplex or Duplex
Unicast
2.2 Designs and Structures of Network Topologies

## Slide 29
Subtopic 1
Bus Topology
Bus topology is a network configuration where all devices are connected to a single main communication cable, often referred to as the "bus" or backbone.
Methods
Broadcast, as there is no direct connection between any pair of end-system.
Benefits
The network's robustness is evident as a malfunction in an individual end-system or its connecting link doesn't impact the network's usability for other end-systems.
2.2 Designs and Structures of Network Topologies

## Slide 30
Subtopic 1
Mesh Topology
Mesh topology is a network arrangement where devices are interconnected with every other device for redundancy and robustness.
Modes
Duplex
Methods
Unicast, Multicast, and Broadcast
Usage
Useful to connect individual LAN/Routers in the network.
2.2 Designs and Structures of Network Topologies

## Slide 31
Subtopic 1
Star Topology
Star topology is a network configuration where devices are connected to a central hub or switch for communication.
Modes
Duplex
Methods
Unicast, Multicast, and Broadcast
Benefits
The malfunction of one end system or its connection doesn't impact the other end systems. However, the central device must not fail.
point-to-point connection
point-to-point connection
Central Device
A specialised device (eg. Switch) with the purpose of connecting other devices in the network. Currently, the star topology is the usual way to configure a network.
2.2 Designs and Structures of Network Topologies

## Slide 32
Subtopic 1
Hybrid network
A hybrid network is a combination of different network topologies, technologies, or architectures, aimed at achieving specific performance, scalability, or redundancy goals.
Advantages: Establish a new LAN with a different topology when using the current topology for the new LAN isn't practical within existing LANs.
2.2 Designs and Structures of Network Topologies

## Slide 33
2.3 Network Transmission Media
Overview
Twisted pair
Cable
Wireless
Coaxial
Fibre-optic
Microwave
Infrared
Radio

## Slide 34
Cable
A transmission using copper wire or fibre-optic.
Twisted pair
Coaxial
Fibre-optic
Factors that need to be considered when selecting cable.
Cost
Bandwidth or data rate
Interference
Need for repeaters
Attenuation at high frequency
2.3 Network Transmission Media

## Slide 35
 | Twisted Pair | Coaxial | Fibre-optic
Diagram |  |  | 
Plastic Jacket
Central Core
Metallic Shield
Dielectric Insulator
Cable
Typically employed to link telephone handsets with telephone lines. Also used in high speed LAN.
Used extensively by cable television companies and in metropolitan network.
The technology of choice for long-distance cabling.
2.3 Network Transmission Media

## Slide 36
 | Twisted Pair | Coaxial | Fibre-optic
Cost | Lowest | Higher | Highest
Bandwidth or data rate | Lowest | Higher | Much higher
Attenuation at high frequency | Affected | Most Affected | Least Affected
Interference | Worst Affected | Less Affected | Least Affected
Need for repeaters | More Often | More Often | Less Often
Cable
2.3 Network Transmission Media

## Slide 37
Wireless
The three choices available are radio, microwave, and infrared, all of which serve as instances of electromagnetic radiation.
Increasing wavelength
Increasing frequency
Radiowaves
Microwaves
Infrared
Visible
Light
Ultraviolet
X rays
Gamma rays
2.3 Network Transmission Media

## Slide 38
Wireless
Microwave
Infrared
Radio
When considering which wireless option to use, you need to consider all of the same factors that were discussed when comparing different kinds of cable.
Cost
Bandwidth or data rate
Interference
Need for repeaters
Attenuation at high frequency
2.3 Network Transmission Media

## Slide 39
 | Radio | Microwave | Infrared
Frequency | 3kHz - 3GHz | 3 - 300 GHz | 300 GHz- 400 THz
Bandwidth or data rate | 3rd | 2nd | 1st
Attenuation due to rain | 3rd | 2nd | 1st
Need for repeaters | 3rd | 2nd | 1st
Directional focusing capability | 3rd | 2nd | 1st
Penetration through a wall | 1st | 2nd | 3rd
only suitable for indoor applications
good for long distance communication
2.3 Network Transmission Media

## Slide 40
 | Cable | Wireless
Permission | Placing cables on the ground necessitates obtaining approval from landholders. | Government agencies control the utilization of specific wireless frequencies through regulations.
Global Communications | Transmission through fibre-optic cables laid underground or seabed | Satellite transmission.
Level of Interference | Lower | Higher
Usage of Repeaters | More Often | Seldom
Mobile Phone Prevalence | Not possible | The only way for phones to access the internet
Comparing cable and wireless transmission
2.3 Network Transmission Media

## Slide 41
Satellites
  They are the components of modern communication systems.
  A satellite has the capability to function as a constituent within a network, establishing direct connections with components situated on the ground.
Low Earth Orbit
Medium Earth Orbit
Geostationary Earth Orbit
  Circling above the equator, these orbits serve the purpose of offering extended telephone and computer network communication.
  They revolve at the Earth's rotational velocity.
  Merely three GEO satellites are essential for complete worldwide coverage."
  Provide the Global Positioning System (GPS).
  Ten MEO are needed for global coverage.
  Functioning in constellations to complement mobile phone networks.
  Complete worldwide coverage necessitates fifty Low Earth Orbit (LEO) satellites.
2.3 Network Transmission Media

## Slide 42
2.4 LAN Hardware components
Wired LAN
Highlighter
Eg. Bus Topology
  Ensure data continuity by preventing signals from reflecting back down the bus.

## Slide 43
Wired LAN
Highlighter
Eg. Bus Topology
Repeater
A device that links two cables while delivering a signal at maximum strength to the second cable.
A repeater accepts an input signal and generates a new signal at full strength.
2.4 LAN Hardware components

## Slide 44
Wired LAN
2.4 LAN Hardware components

## Slide 45
Wired LAN
Bridge
Segment 1
Segment 2
2.4 LAN Hardware components

## Slide 46
Segment 1 | Segment 2
00:1A:2B:3C:4D:5E | 2A:B7:EF:53:19:C8
08:00:27:3D:8A:BF | 40:72:A9:ED:6F:51
12:34:56:78:90:AB | 5E:F8:C3:0A:97:BB
1C:6F:22:9D:F0:E5 | 
Wired LAN
Bridge
Segment 1
Segment 2
An device that links two segments of a Local Area Network (LAN).
2.4 LAN Hardware components

## Slide 47
Wired LAN
Network Interface Card
A Network Interface Card (NIC) is a hardware component that enables devices to connect and communicate within a network.
It has a unique address that is used to identify the end-system which it has been installed.
2.4 LAN Hardware components

## Slide 48
Wired LAN
Eg. Star Topology
The central device might be a hub, switch or a router.
2.4 LAN Hardware components

## Slide 49
  Also known as WLAN, WiFi
  Formal Description IEEE 802.11, wireless LAN standard that uses radio frequency transmission.
  Central Device: Wireless Access Point (WAP)
  The Wireless Access Point (WAP) is capable of establishing communication with an end-system, given that the end-system is equipped with a Wireless Network Interface Card.
Wireless LAN
2.4 LAN Hardware components

## Slide 50
2.5 Ethernet Technology and Standards
Definition
Ethernet is a networking technology encompassing protocols, ports, cables, and computer chips essential for connecting desktops or laptops to local area networks (LANs). This enables high-speed data transmission using coaxial or fiber optic cables.
Alternative name:
IEEE 802.3
Data Speed Capability
100 gigabit
Institute of Electrical and Electronics Engineers (IEEE)

## Slide 51
Ethernet
Ethernet was deployed in a local area network (LAN) that could be structured as a bus or a star, with a hub acting as the central device. In both arrangements, data transmission utilized a broadcast approach.
Bus Topology
Star Topology
2.5 Ethernet Technology and Standards

## Slide 52
Collision
Employing a shared medium for transmitting messages introduces the possibility of message corruption during the transmission process. If two end-systems attempt to transmit messages simultaneously, a situation known as a 'collision' occurs.
Bus Topology
Send!
Send!
2.5 Ethernet Technology and Standards

## Slide 53
Collision
Employing a shared medium for transmitting messages introduces the possibility of message corruption during the transmission process. If two end-systems attempt to transmit messages simultaneously, a situation known as a 'collision' occurs.
Bus Topology
Send!
Send!
message
message
2.5 Ethernet Technology and Standards

## Slide 54
Solution - CSMA/CD
(Carrier sense multiple access with collision detection)
Transmitter checks the voltage on the transmission medium.
When a message was in transit, a detectable voltage level was present on the Ethernet cable, and this could be sensed by an end-system.
Bus Topology
Send!
Send!
Voltage!
2.5 Ethernet Technology and Standards

## Slide 55
Solution - CSMA/CD
(Carrier sense multiple access with collision detection)
Transmitter checks the voltage on the transmission medium.
When a message was in transit, a detectable voltage level was present on the Ethernet cable, and this could be sensed by an end-system.
If this indicates activity, wait a random time before checking again.
Bus Topology
Send!
Send!
Voltage!
2.5 Ethernet Technology and Standards

## Slide 56
Solution - CSMA/CD
(Carrier sense multiple access with collision detection)
Transmitter checks the voltage on the transmission medium.
When a message was in transit, a detectable voltage level was present on the Ethernet cable, and this could be sensed by an end-system.
Continuously check for a collision. If no collision is detected, continue transmission.
If no activity is detected, start transmission.
Bus Topology
Send!
Send!
Voltage!
2.5 Ethernet Technology and Standards

## Slide 57
Solution - CSMA/CD
(Carrier sense multiple access with collision detection)
Transmitter checks the voltage on the transmission medium.
When a message was in transit, a detectable voltage level was present on the Ethernet cable, and this could be sensed by an end-system.
If no activity is detected, start transmission.
If collision is detected, stop transmission of the message and transmit a jamming signal to warn all end-stations; after a random time, try again.
Bus Topology
Send!
Send!
Voltage!
2.5 Ethernet Technology and Standards

## Slide 58
Ethernet - Star Topology
No collision is possible in this case.
Due to the possibility of significant activity, the switch must have the capability to store an incoming message in a buffer until the cable becomes available for transmission to occur.
Star Topology
Switch
2.5 Ethernet Technology and Standards

## Slide 59
Subtopic 1
2.6 Architecture of the Internet
The Internet
=Internetwork
Local Area Network (LAN)

## Slide 60
Subtopic 1
The Internet
=Internetwork
Local Area Network (LAN)
Local Area Network (LAN)
Local Area Network (LAN)
2.6 Architecture of the Internet

## Slide 61
Subtopic 1
The Internet
=Internetwork
Every single network on Earth.
but .. what infrastructure needs to be in place?
2.6 Architecture of the Internet

## Slide 62
Subtopic 1
Internet Service Provider (ISP)
An Internet Service Provider (ISP) is an entity that offers individuals and organizations access to the internet, providing services like connectivity and web-related features. ISPs enable users to connect to and utilize the global network of interconnected computers and resources.
Access ISP
Give internet access to an individual or company.
2.6 Architecture of the Internet

## Slide 63
Subtopic 1
Internet Service Provider (ISP)
Region ISP = Connect states / regions
Access ISP
Regional ISP
Access ISP
Access ISP
2.6 Architecture of the Internet

## Slide 64
Subtopic 1
Internet Service Provider (ISP)
Backbone ISP = Connect countries
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
2.6 Architecture of the Internet

## Slide 65
Subtopic 1
Internet Service Provider (ISP)
Backbone ISP = Connect countries
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Access ISP
Regional ISP
Access ISP
Access ISP
Backbone ISP
2.6 Architecture of the Internet

## Slide 66
Subtopic 1
fibre-optic cable
underground
fibre-optic cable seabed
Router
Mesh Configuration: The cable mesh consists of numerous connection points known as nodes, featuring routers at each node.
Router Function: Routers are present not just in the broader internet mesh but also within ISP networks.
Interconnectivity: Each router links with multiple other routers, responsible for determining the optimal transmission path.
Route Selection: Routers decide the most suitable route for data transmission, aiding efficient network communication.
2.6 Architecture of the Internet

## Slide 67
Subtopic 1
Public switched telephone network (PSTN)
The Public Switched Telephone Network (PSTN) was primarily designed to provide infrastructure support for voice communication over traditional landline telephones. However, its underlying infrastructure has played a role in supporting early stages of internet connectivity in the past, particularly during the dial-up era.
2.6 Architecture of the Internet

## Slide 68
Subtopic 1
Public switched telephone network (PSTN)
Dial-Up Internet Access: Before broadband technologies became widespread, dial-up internet access was a common method for connecting to the internet. In a dial-up connection, a computer uses a modem to establish a connection over a standard telephone line through the PSTN. The modem translates digital data from the computer into analog signals that can be transmitted over the analog PSTN infrastructure. This connection allowed users to access the internet, albeit at slower speeds compared to modern broadband connections.
2.6 Architecture of the Internet

## Slide 69
Subtopic 1
Evolution of PSTN
In more recent times, PSTNs have enhanced their primary communication pathways using fiber-optic cables and digital technology. This upgrade has enabled them to enhance leased line offerings to ISPs and has also opened the door for them to provide their own ISP services.
They offer two services:
Broadband network connection
Wifi Hotspot Technology
2.6 Architecture of the Internet

## Slide 70
Subtopic 1
Cell Phone Network
Users of mobile-capable devices have an alternative method to access the internet through mobile companies that function as ISPs. Using suitable software, the mobile phone communicates with a regular cell tower, allowing access to the wireless phone network, subsequently establishing a connection to the internet.
2.6 Architecture of the Internet

## Slide 71
1 - The World Wide Web
2.7 Internet-Based Applications
The World Wide Web is not the internet.
The World Wide Web (WWW) is an application accessible over the internet.

## Slide 72
2 - Cloud Computing
Cloud computing is a technology model that provides on-demand access to a shared pool of computing resources, such as servers, storage, applications, and services, over the internet.
2.7 Internet-Based Applications

## Slide 73
2 - Cloud Computing
Cloud computing is a technology model that provides on-demand access to a shared pool of computing resources, such as servers, storage, applications, and services, over the internet.
Private Cloud
Public Cloud
2.7 Internet-Based Applications

## Slide 74
2 - Cloud Computing
Private Cloud
Public Cloud
A private cloud is a dedicated and isolated cloud computing environment that serves a single organization and is not shared with other users. There are three possible approaches:
The organization assumes complete accountability for establishing and overseeing the on-premises cloud infrastructure linked to an exclusive network.
The organization delegates the task of setting up and administering an
on-premises installation connected to a private network to a third-party provider.
The organisation outsources the creation and management of an Internet accessible system by a third-party.
2.7 Internet-Based Applications

## Slide 75
Platform provision
Software provision
2 - Cloud Computing
Public Cloud
Private Cloud
A public cloud is a shared computing environment provided by a third-party vendor, accessible over the internet to multiple users and organizations.
Enabled by:
Using large mainframe computers or server farms.
Service provided:
Infrastructure provision
Azure App Services
Amazon EC2
2.7 Internet-Based Applications

## Slide 76
Public Cloud
Advantages
Infrastructure provision
Platform provision
Software provision
Improved software performance and expanded storage capacity.
Provide resources and environments for the purpose of software development and testing.
The cloud will be able to run applications that require high performance systems. Save money as company does not have Toby a software package. Users do not need technical expertise.
Disadvantage
The cloud service provider maintains full access to all data stored in the cloud, leading to uncertainty for the cloud user about the possibility of their data being shared with third parties.
Data Privacy
2.7 Internet-Based Applications

## Slide 77
3 - Bit Streaming
A bitstream is a sequential series of binary digits (bits) that represents digital data, including video, and is used for transmission, storage, and processing.
0101011001001
2.7 Internet-Based Applications

## Slide 78
Media Streaming
2.7 Internet-Based Applications

## Slide 79
Media Streaming
Download
On Demand
Real-time
James Gan
2.7 Internet-Based Applications

## Slide 80
Media Streaming
Download
On Demand
Real-time
User will download content from the server then listen to it / watch it at some future convenient time.
2.7 Internet-Based Applications

## Slide 81
Media Streaming
Buffer
Download
On Demand
When the user selects a specific moment for transmitting the content of the bitstream.
Real-time
010101010
010010111
2.7 Internet-Based Applications

## Slide 82
Media Streaming
Download
On Demand
Real-time
As the bitstream content is generated, it is simultaneously transmitted.
Because many users might be watching the content at the same time, the media is first sent to lots of content provider servers, and then these servers send it to individual users.
james gan
2.7 Internet-Based Applications

## Slide 83
Term- Bit Rate
The number of bits transmitted per second.
1Mb / s
Bit rate has to be > 1 Mb /s for a good viewing experience
2.7 Internet-Based Applications

## Slide 84
Term- Bit Rate
The bit rate is limited by the bandwidth of the network connection.
2.7 Internet-Based Applications

## Slide 85
Term- Buffer
The stored media file that has not been played.
It is essential to have a buffer size that is sufficiently large for it to never get filled.
010101010
010010111
Indicates the minimum amount of data in the buffer before it triggers a data addition process.
High-water mark
Low-water mark
Indicate the maximum amount of data the buffer can hold before it triggers a pause or data removal process.
2.7 Internet-Based Applications

## Slide 86
Term- Buffer
The stored media file that has not been played.
Indicates the minimum amount of data in the buffer before it triggers a data addition process.
High-water mark
Low-water mark
Indicate the maximum amount of data the buffer can hold before it triggers a pause or data removal process.
2.7 Internet-Based Applications

## Slide 87
Term- Buffer
The media player continuously monitors how full the buffer is and controls the bit rate in relation to the defined high-and low-water marks.
Indicates the minimum amount of data in the buffer before it triggers a data addition process.
High-water mark
Low-water mark
Indicate the maximum amount of data the buffer can hold before it triggers a pause or data removal process.
2.7 Internet-Based Applications

## Slide 88
2.8 IP Addressing and Network Identification
IPv4 addressing
Used to define from where and to where data is being transmitted.
Send to:
192.168.1.1
192.168.1.1
192.168.1.2

## Slide 89
Format
  32 bits / 4 bytes
  Allows for 2 addresses
Binary
32
.
.
.
11000000
10101000
00000001
00001010
.
.
.
192
168
1
10
Denary
2.8 IP Addressing and Network Identification

## Slide 90
Original Scheme
The initial addressing system was created using a hierarchical structure where
  A set of bits determined a network (netID)
  A set of bits determined a host within that network (hostID)
  A set of bits determined a class
Highlighter
.
0
7 bits
.
10
14 bits
.
110
21 bits
Class A
Class B
Class C
.
.
24 bits
.
16 bits
.
8 bits
Identifier
netID
hostID
2.8 IP Addressing and Network Identification

## Slide 91
Original Scheme
The initial addressing system was created using a hierarchical structure where
  A set of bits determined a network (netID)
  A set of bits determined a host within that network (hostID)
  A set of bits determined a class
Highlighter
.
0
0001010
.
10
10110000010000
.
110
000001010100000000000
Class A
Class B
Class C
.
.
000000000000000000000001
.
0000000000000001
.
00000001
Identifier
netID
hostID
2.8 IP Addressing and Network Identification

## Slide 92
Original Scheme
Highlighter
.
0
0001010
Class A
.
000000000000000000000001
Identifier
netID
hostID
Allows initial transmission to be routed.
Will only need to be examined on arrival at the identified network.
2.8 IP Addressing and Network Identification

## Slide 93
Problems with the original scheme
The issue emerged as local area networks (LANs) became widespread. There was a shortage of available Class B network IDs, and if organizations were assigned to Class C, the available number of host IDs became inadequate.
.
10
14 bits
.
110
21 bits
Class B
Class C
.
16 bits
.
8 bits
2 = 16384
2 = 256
14
8
2.8 IP Addressing and Network Identification

## Slide 94
Classless inter-domain routing
.
0
7 bits
.
10
14 bits
.
110
21 bits
Class A
Class B
Class C
.
24 bits
.
16 bits
.
8 bits
Identifier
netID
hostID
2.8 IP Addressing and Network Identification

## Slide 95
Classless inter-domain routing
How? Add an 8-bit suffix to the address that specifies the number of bits for the netID.
For example, let’s say we want our netID to have a length of 18 (hence our hostID will have a length of 14).
Highlighter
00001010.00000000.01000000.00000000
Dotted decimal notation:
10
0
64
0
/ 18
2.8 IP Addressing and Network Identification

## Slide 96
Classless inter-domain routing
How? Add an 8-bit suffix to the address that specifies the number of bits for the netID.
For example, let’s say we want our netID to have a length of 18 (hence our hostID will have a length of 14).
Highlighter
00001010.00000000.01000000.00000000
Dotted decimal notation:
10
0
64
0
/ 18
first 18 bits:
netID
last 14 bits:
hostID
2.8 IP Addressing and Network Identification

## Slide 97
Benefits of CIDR
CIDR allows us to use variable-length subnet masks, which means we can allocate IP addresses in a more flexible and efficient manner. This is super important in today's internet where we're running out of IPv4 addresses. With CIDR, we can allocate just the right amount of addresses to different networks, preventing address wastage and improving overall IP address utilization.
2.8 IP Addressing and Network Identification

## Slide 98
Sub-netting
Highlighter
Subnetting is the process of dividing a larger network into smaller, more manageable sub-networks to improve efficiency and organization in IP address allocation and routing.
Sub-networks
Network
Network
2.8 IP Addressing and Network Identification

## Slide 99
Sub-netting
Highlighter
Example:
A school that wants to accommodate 200 workspaces, and they have 8 departments
D1
D2
D3
D4
D5
D6
D7
D8
The school will need eight individual Class C netIDs; one for each LAN.
24 bits
.
8 bits
first 24 bits:
netID
last 8 bits:
hostID
for each department
= 256 workspaces for each department
2.8 IP Addressing and Network Identification

## Slide 100
Sub-netting
Example:
A school that wants to accommodate 250 workspaces, and they have 8 departments
D1
D2
D3
D4
D5
D6
D7
D8
8 departments x 256 addresses
= 2048 addresses
Wasted Addresses
2048 - 200
= 1848 addresses
We need to solve this
2.8 IP Addressing and Network Identification

## Slide 101
Sub-netting
D1
D2
D3
D4
D5
D6
D7
D8
Solution: Let all the departments share one netID.
24 bits
3 bits
first 24 bits:
netID
8 bits
5 bits
last 8 bits:
hostID
000
001
010
011
100
101
110
111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
= 32 addresses x 8
= 256 addresses
2.8 IP Addressing and Network Identification

## Slide 102
Sub-netting
D1
D2
D3
D4
D5
D6
D7
D8
24 bits
3 bits
first 24 bits:
netID
8 bits
5 bits
last 8 bits:
hostID
000
001
010
011
100
101
110
111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
00000 - 11111
= 32 addresses x 8
= 256 addresses
D1
D2
D3
D4
D5
D6
D7
D8
No subnetting
Subnetting
Wasted Addresses
2048 - 200
= 1848 addresses
Wasted Addresses
256 - 200
= 56 addresses
24 bits
.
8 bits
24 bits
.
8 bits
24 bits
.
8 bits
24 bits
.
8 bits
24 bits
.
8 bits
24 bits
.
8 bits
24 bits
.
8 bits
24 bits
.
8 bits
2.8 IP Addressing and Network Identification

## Slide 103
Network Address Translation (NAT)
Highlighter
NAT allows multiple devices in a private network to access the internet using a single public IP address.
NAT 1
NAT 2
NAT 3
203.0.113.45
151.101.65.121
8.8.8.8
2.8 IP Addressing and Network Identification

## Slide 104
Network Address Translation (NAT)
NAT 1
NAT 2
NAT 3
203.0.113.45
151.101.65.121
8.8.8.8
Internet Router
NAT allows multiple devices in a private network to access the internet using a single public IP address.
2.8 IP Addressing and Network Identification

## Slide 105
Network Address Translation (NAT)
NAT 1
NAT 2
NAT 3
203.0.113.45
151.101.65.121
8.8.8.8
Internet Router
Private IP Address
192.168.1.10
10.0.2.25
172.16.0.100
192.168.1.10
10.0.2.25
172.16.0.100
192.168.1.10
10.0.2.25
172.16.0.100
They can be the same! Does not have to be unique.
2.8 IP Addressing and Network Identification

## Slide 106
Private Address Range
10.0.0.0
172.16.0.0
192.168.0.0
10.255.255.255
172.31.255.255
192.168.255.255
Range
Range
Range
2.8 IP Addressing and Network Identification

## Slide 107
Network Address Translation (NAT)
NAT 1
203.0.113.45
  The NAT box's interface is equipped with software that analyzes every inbound and outbound communication.
  A security assessment can occur prior to routing an incoming transmission to the appropriate internal address.
2.8 IP Addressing and Network Identification

## Slide 108
Static and Dynamic Address
When a user desires to access the internet, the responsibility of managing the connection falls on an Internet Service Provider.
There are instances where the ISP might be accommodating more users than the total count of available addresses. This is when a dynamic address is needed.
Dynamic Address
Static Address
An automatically assigned network identifier that changes periodically as devices connect and disconnect
A fixed, unchanging network identifier assigned to a device, often used for consistent hosting or management purposes.
2.8 IP Addressing and Network Identification

## Slide 109
IPv6 Addressing
IPv4's limited pool of available addresses is insufficient to accommodate the growing number of devices and users on the internet in this decade, necessitating the adoption of IPv6 with its vastly expanded address space.
IPv6 Address Format
128 bits
Written in colon hexadecimal notation
3ffe : 1900 : 4545 : 3a7b: 200a : f8ff : fe21 : 67cf
Eg:
2.8 IP Addressing and Network Identification

## Slide 110
2.9 Domain Name System
Domain Name System
DNS (Domain Name System) is a decentralized naming system that translates human-readable domain names into IP addresses, facilitating internet communication.
www.abc.com
151.101.65.121

## Slide 111
2.9 Domain Name System
Domain Name System
The DNS (Domain Name System) is structured hierarchically, resembling an upside-down tree.
Root servers
Top Level Domains
Top of hierarchy, starting point for DNS queries.
.com, .org, .net, and country-code TLDs like .us, .uk, etc.
Second-Level Domains
Beneath the TLDs are the second-level domains, which are the actual domains that people typically register, like google.com or example.org
more levels ...

## Slide 112
2.9 Domain Name System
Root servers
Top Level Domains
Second-Level Domains
more levels ...
Name Resolution
Process to look up a domain name to find an IP address. There are 3 outcomes.
If the server receiving the query has control over the domain, it provides an accurate and authoritative IP address in response.
For remote domains in a query, it's sent to a root server that gives the top-level domain's name server address, leading to the next lower domain's name server, and so on, until an authoritative IP address is obtained.
Even if the server doesn't control the domain, it can provide an IP address from its cache of recent requests, which might be outdated.
james gan