## Slide 1
Cambridge International AS Level Computer Science (9618) – Revision Notes
This pack is intended for students to who are taking CIE AS Level in Computer Science, either in preparation for their AS exam, or more likely alongside year 2 of the course to improve fluency, recall and pace on AS topics. It could be used as lesson starters, or supplied to students for independent use.
Monitoring and Control System

## Slide 2
Monitoring and Control System
A LEVEL COMPUTER SCIENCE
Chapter
7

## Slide 3
Chapter
Outline
Monitoring System
7.1
Control Systems
7.2
Bit manipulation
7.3

## Slide 4
7.1 Monitoring System
A monitoring system is a tool that continuously observes and tracks the performance of various components, providing real-time data and alerts for proactive management and problem resolution.
Structure
Definition
Highlighter
Sensor
Computer / Microprocessor
Warning
Detect real- time data
Check if data is out of range
Types of sensor
Temperature
Humidity
pH
Light

## Slide 5
7.1 Monitoring System
Motion Sensor
Computer / Microprocessor
Sound an alarm
Home Security Monitoring System
Security Camera
When it detects unusual motion or a breach of a door/window:

## Slide 6
7.1 Monitoring System
Computer / Microprocessor
Thermocouples placed within industrial machinery or processes
Industrial Temperature Monitoring System
When it detects a temperature outside the acceptable range:
Need to shut down the equipment!

## Slide 7
7.1 Monitoring System
Computer / Microprocessor
Incorporates a variety of sensors including ECG (Electrocardiogram) for heart activity, pulse oximeters for blood oxygen levels, blood pressure cuffs for blood pressure,
Hospital Patient Monitoring System
When the system detects abnormal vital signs or deviations from the preset thresholds, it can trigger alarms, alert healthcare providers, and display the patient's data on a central monitoring station.

## Slide 8
Subtopic 1
7.2 Control System
A control system has the monitoring activity plus the capability to control a system.
Structure
Definition
Sensor
Computer / Microprocessor
Detect real- time data
Check if data is out of range
Types of sensor
Temperature
Humidity
pH
Light
Do something with an actuator
An actuator is a mechanical or electronic device that is responsible for converting a control signal into a physical action or movement, often used to adjust or manipulate a system or its components.

## Slide 9
Subtopic 1
7.2 Control System
Schematic Diagram
Controlled environment
Sensor
Actuator
Analogue to Digital Converter
ADC
37 c
o
100101
Computer or Microprocessor
Digital control signal
Digital to Analogue Converter
DAC
Analogue control signal

## Slide 10
Subtopic 1
7.2 Control System
  The computer will signal the sensor at scheduled intervals to obtain a measurement.
Controlled environment
Sensor
Actuator
Analogue to Digital Converter
ADC
37 c
o
100101
Computer or Microprocessor
Digital control signal
Digital to Analogue Converter
DAC
Analogue control signal

## Slide 11
Subtopic 1
7.2 Control System
2. When the computer receives a measurement value that falls outside the desired range, it triggers a control action.
Controlled environment
Sensor
Actuator
Analogue to Digital Converter
ADC
37 c
o
100101
Computer or Microprocessor
Digital control signal
Digital to Analogue Converter
DAC
Analogue control signal
Out of range, take action!

## Slide 12
Subtopic 1
7.2 Control System
3. The subsequent timed measurement will occur after the execution of this control action. Essentially, the next timed measurement offers feedback to the computer regarding the impact of the control action.
Controlled environment
Sensor
Actuator
Analogue to Digital Converter
ADC
37 c
o
100101
Computer or Microprocessor
Digital control signal
Digital to Analogue Converter
DAC
Analogue control signal
Out of range, take action!

## Slide 13
Subtopic 1
7.2 Control System
Controlled environment
Sensor
Actuator
Analogue to Digital Converter
ADC
37 c
o
100101
Computer or Microprocessor
Digital control signal
Digital to Analogue Converter
DAC
Analogue control signal
Closed-loop feedback system

## Slide 14
Subtopic 1
7.2 Control System
Controlled environment
Temperature
Sensor
Actuator
Analogue to Digital Converter
ADC
10 c
o
Computer or Microprocessor
Digital to Analogue Converter
DAC
Thermostat in a Home Heating System
If the temperature falls below the setpoint ...
The thermostat sends a signal to the heating system to increase the heat output!

## Slide 15
Subtopic 1
7.2 Control System
Controlled environment
Speed Sensor
Actuator
Analogue to Digital Converter
ADC
1000 m/s
Computer or Microprocessor
Digital to Analogue Converter
DAC
Automotive Cruise Control System
If the vehicle's speed deviates from the set cruise speed
The system adjusts the throttle or brakes to bring the speed back to the desired level.

## Slide 16
Subtopic 1
7.2 Control System
Controlled environment
Blood glucose Sensor
Actuator
Analogue to Digital Converter
ADC
37 c
o
Computer or Microprocessor
Digital to Analogue Converter
DAC
Blood Glucose Monitoring System for Diabetics
When the sensor detects a blood glucose level outside the desired range ...
It administers insulin or suggests dietary changes to regulate blood sugar levels

## Slide 17
7.3 Bit Manipulation
A real-time program must run continuously, and this program can assign values to Boolean variables based on the sensor data.
High Temperature
Controlled environment
Sensor
Actuator
Analogue to Digital Converter
ADC
37 c
o
100101
Computer or Microprocessor
Digital control signal
Digital to Analogue Converter
DAC
Analogue control signal
Low Temperature
1
0
We need a way to set the bits!
(Bit manipulation)

## Slide 18
7.3 Bit Manipulation
A real-time program must run continuously, and this program can assign values to Boolean variables based on the sensor data.
High Temperature
Controlled environment
Sensor
Actuator
Analogue to Digital Converter
ADC
37 c
o
100101
Computer or Microprocessor
Digital control signal
Digital to Analogue Converter
DAC
Analogue control signal
Low Temperature
1
0
We need a way to set the bits!
(Bit manipulation)
Setting all the bits to 0.
(Useful when restarting a system)
Setting a bit to 1 regardless of its current value (Useful to report a condition)
Toggle the value of one bit (Useful when changing the value of a flag)
Setting all bits to zero except one bit which is of interest

## Slide 19
7.3 Bit Manipulation
Setting all the bits to 0.
(Useful when restarting a system)
Illustration
20
17
11010011
18
19
ACC
10011101
11010011
11100111
LDD 17
Assembly Language
AND #B00000000
STO 17
The following code will set all the bits at <17> to 00000000

## Slide 20
7.3 Bit Manipulation
Illustration
20
17
11010011
18
19
10011101
ACC
10011101
11010011
11100111
LDD 17
Assembly Language
AND #B00000000
STO 17
The following code will set all the bits at <17> to 00000000
Setting all the bits to 0.
(Useful when restarting a system)

## Slide 21
1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
7.3 Bit Manipulation
Illustration
20
17
11010011
18
19
10011101
ACC
10011101
11010011
11100111
LDD 17
Assembly Language
AND #B00000000
STO 17
The following code will set all the bits at <17> to 00000000
AND
Setting all the bits to 0.
(Useful when restarting a system)

## Slide 22
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
7.3 Bit Manipulation
Illustration
20
17
11010011
18
19
00000000
ACC
10011101
11010011
11100111
LDD 17
Assembly Language
AND #B00000000
STO 17
The following code will set all the bits at <17> to 00000000
Setting all the bits to 0.
(Useful when restarting a system)

## Slide 23
7.3 Bit Manipulation
Illustration
20
17
11010011
18
19
00000000
ACC
00000000
11010011
11100111
LDD 17
Assembly Language
AND #B00000000
STO 17
The following code will set all the bits at <17> to 00000000
Setting all the bits to 0.
(Useful when restarting a system)

## Slide 24
7.3 Bit Manipulation
Illustration
20
17
1101001
18
19
ACC
00000000
11010011
11100111
LDD 18
Assembly Language
XOR #B00000001
STO 18
The following code will toggle the 1th bit of the content at <18>
Toggle the value of one bit (Useful when changing the value of a flag)
1

## Slide 25
7.3 Bit Manipulation
Illustration
20
17
1101001
18
19
1101001
ACC
00000000
11010011
11100111
LDD 18
Assembly Language
XOR #B00000001
STO 18
The following code will toggle the 1th bit of the content at <18>
Toggle the value of one bit (Useful when changing the value of a flag)
1
1

## Slide 26
7.3 Bit Manipulation
Illustration
20
17
1101001
18
19
1101001
ACC
00000000
11010011
11100111
LDD 18
Assembly Language
XOR #B00000001
STO 18
The following code will toggle the 1th bit of the content at <18>
Toggle the value of one bit (Useful when changing the value of a flag)
1
1
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
XOR

## Slide 27
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
7.3 Bit Manipulation
Illustration
20
17
1101001
18
19
1101001
ACC
00000000
11010011
11100111
LDD 18
Assembly Language
XOR #B00000001
STO 18
The following code will toggle the 1th bit of the content at <18>
Toggle the value of one bit (Useful when changing the value of a flag)
1
1
XOR
Nothing change!

## Slide 28
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
11010011
11100111
LDD 18
Assembly Language
XOR #B00000001
STO 18
The following code will toggle the 1th bit of the content at <18>
Toggle the value of one bit (Useful when changing the value of a flag)
11010010

## Slide 29
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
11010011
1110011
LDD 19
Assembly Language
OR #B00000001
STO 19
The following code will toggle the 1th bit of the content at <19> to 1 regardless of its current value.
Setting a bit to 1 regardless of its current value (Useful to report a condition)
1

## Slide 30
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
11010011
1110011
LDD 19
Assembly Language
OR #B00000001
STO 19
The following code will toggle the 1th bit of the content at <19> to 1 regardless of its current value.
Setting a bit to 1 regardless of its current value (Useful to report a condition)
1110011
1
1

## Slide 31
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
11010011
1110011
LDD 19
Assembly Language
OR #B00000001
STO 19
The following code will toggle the 1th bit of the content at <19> to 1 regardless of its current value.
Setting a bit to 1 regardless of its current value (Useful to report a condition)
1110011
1
1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
OR

## Slide 32
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
11010011
LDD 19
Assembly Language
OR #B00000001
STO 19
The following code will toggle the 1th bit of the content at <19> to 1 regardless of its current value.
Setting a bit to 1 regardless of its current value (Useful to report a condition)
11100111
11100111

## Slide 33
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
110100 1
LDD 20
Assembly Language
AND #B00000010
STO 20
The following code will set all the bits to zero except for the 2nd bit. At the end of the operation, a comparison can be made with the binary value to check if the bit is set (whether it is a ‘1’ or ‘0’).
Setting all bits to zero except one bit which is of interest
11100111
1

## Slide 34
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
110100 1
LDD 20
Assembly Language
AND #B00000010
STO 20
The following code will set all the bits to zero except for the 2nd bit. At the end of the operation, a comparison can be made with the binary value to check if the bit is set (whether it is a ‘1’ or ‘0’).
Setting all bits to zero except one bit which is of interest
110100 1
11100111
1
1

## Slide 35
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
110100 1
LDD 20
Assembly Language
AND #B00000010
STO 20
The following code will set all the bits to zero except for the 2nd bit. At the end of the operation, a comparison can be made with the binary value to check if the bit is set (whether it is a ‘1’ or ‘0’).
Setting all bits to zero except one bit which is of interest
110100 1
11100111
1
1
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
AND

## Slide 36
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
110100 1
LDD 20
Assembly Language
AND #B00000010
STO 20
The following code will set all the bits to zero except for the 2nd bit. At the end of the operation, a comparison can be made with the binary value to check if the bit is set (whether it is a ‘1’ or ‘0’).
Setting all bits to zero except one bit which is of interest
00000010
11100111
1

## Slide 37
7.3 Bit Manipulation
Illustration
20
17
11010010
18
19
ACC
00000000
00000010
LDD 20
Assembly Language
AND #B00000010
STO 20
The following code will set all the bits to zero except for the 2nd bit. At the end of the operation, a comparison can be made with the binary value to check if the bit is set (whether it is a ‘1’ or ‘0’).
Setting all bits to zero except one bit which is of interest
00000010
11100111
This can be compared to the denary value #2 to check if the 2th bit is set (whether it is equal to ‘1’).

## Slide 38
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
7.3 Bit Manipulation
Worked Example
The following byte is stored in a register in which the bits can be individually set or cleared. For example:
Highlighter
Could be a flag for sensors to indicate a problem
Could be a flag for actuator to know whether to take actions

## Slide 39
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
7.3 Bit Manipulation
Worked Example
All of the bits need to be set to 0. What logical bitwise operation + operand is required?
Highlighter

## Slide 40
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
7.3 Bit Manipulation
Worked Example
All of the bits need to be set to 0. What logical bitwise operation + operand is required?
Highlighter
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
AND
AND
AND
AND
AND
AND
AND
AND

## Slide 41
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
7.3 Bit Manipulation
Worked Example
All of the bits need to be set to 0. What logical bitwise operation + operand is required?
Highlighter
AND
0000 0000
Bitwise Operation
Operand

## Slide 42
1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
7.3 Bit Manipulation
Worked Example
A sensor has recorded a value that is too high so bit 3 must be set to 1 but other bits must remain unaltered. State which logical bitwise operation + operand is required.
Highlighter

## Slide 43
1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
7.3 Bit Manipulation
Worked Example
A sensor has recorded a value that is too high so bit 3 must be set to 1 but other bits must remain unaltered. State which logical bitwise operation + operand is required.
Highlighter
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
OR
OR
OR
OR
OR
OR
OR
OR
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0

## Slide 44
1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
7.3 Bit Manipulation
Worked Example
A sensor has recorded a value that is too high so bit 3 must be set to 1 but other bits must remain unaltered. State which logical bitwise operation + operand is required.
Highlighter
OR
0010 0000
Bitwise Operation
Operand

## Slide 45
1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
7.3 Bit Manipulation
Worked Example
Bit number 1 and number 8 needs to toggle (0 to 1, 1 to 0) due to a misreading. State which logical bitwise operation + operand is required.
Highlighter

## Slide 46
1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
7.3 Bit Manipulation
Worked Example
Bit number 1 and number 8 needs to toggle (0 to 1, 1 to 0) due to a misreading. State which logical bitwise operation + operand is required.
Highlighter
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
XOR
XOR
XOR
XOR
XOR
XOR
XOR
XOR
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1

## Slide 47
1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
7.3 Bit Manipulation
Worked Example
Bit number 1 and number 8 needs to toggle (0 to 1, 1 to 0) due to a misreading. State which logical bitwise operation + operand is required.
Highlighter
XOR
1000 0001
Bitwise Operation
Operand